## Slide 1
FIRST
3D detection
3D tracking
Trajectory prediction
End-to-end motion
1
2
SiT Dataset: Socially Interactive Pedestrian Trajectory Dataset for Social Navigation Robots
Jongwook Bae, Jungho Kim, Junyong Yun, Changwon Kang, Jeongseon Choi, Chanhyeok Kim, Junho Lee, Jungwook Choi, Jun Won Choi
Hanyang University
Problem
Method
Key Results
Social navigation robots must perceive and predict nearby
pedestrian trajectories to move safely through shared spaces. Yet
existing datasets never capture the close human–robot interaction
a navigating robot actually experiences.
Rooftop-camera and driving datasets keep pedestrians and the
sensor on separate paths.
Motivation
Headline Numbers
Takeaway
Dataset / Benchmark
The dataset, development kit, and trained baselines are all publicly
released — giving social-navigation research the close human–
robot interaction data that driving and fixed-camera datasets lack.
Remotely operated Clearpath Husky UGV with 2× Velodyne
VLP-16 LiDARs, five Basler cameras for full 360° coverage, two
IMUs, and RTK.
A pulse-per-second (PPS) trigger aligns every LiDAR and
camera for precise time synchronization.
Localize — RTK outdoors, LiDAR-inertial SLAM indoors.
Annotate & map — 3D cuboids 5 Hz → 10 Hz, 2D from
shared IDs; 12-layer semantic maps; faces & plates blurred.
SiT clusters pedestrians close & all-around the ego-robot vs. Waymo and
nuScenes.
A robot shares pedestrians' path, provoking close-range
interactive walking behaviors.
Data must come from a robot moving in real crowds with time-
synchronized sensors.
Husky UGV: 5 cameras (360°), 2 LiDARs, 2 IMUs, RTK.
The first robot-in-crowd pedestrian trajectory dataset — synced
multi-modal sensors, semantic maps, and a full perception-to-
prediction benchmark.
60 scenes ≈ 60K images + 12K point clouds; ~470K 2D + ~320K
3D annotations. Each 20 s clip at 10 Hz gives a 9 s trajectory.
360° pedestrian trajectories, point clouds & ego-motion in real crowds.
320K
3D annotations
60K
images
12K
point clouds
0.531
best mAP
0.517
best ADE₂₀