## Slide 1
HANYANG UNIVERSITY
NeurIPS 2023 · Datasets & Benchmarks
SiT Dataset
Socially Interactive Pedestrian Trajectory
for Social Navigation Robots
Trajectories recorded by a robot moving through real crowds —
perceiving and predicting the people around it, up close.
Bae, Kim, Yun, Kang, Choi, Kim, Lee, Choi, Choi
SCAN FOR CODE
github.com/SPALaboratory/SiT-Dataset
Dataset · dev-kit · baselines
released publicly.
WHAT IT IS
The SiT dataset — Socially Interactive Pedestrian
Trajectory — captures genuine human-robot
interaction as a robot navigates crowds.
WHY IT IS NEW
Unlike fixed rooftop cameras or cars on separate
roads, SiT was recorded by a mobile robot in
densely populated indoor and outdoor Seoul.
WHAT IT SHIPS
Synchronized LiDAR, camera, IMU and RTK, 2D and 3D
annotations, semantic maps, and a benchmark from
detection to end-to-end forecasting.

## Slide 2
THE PROBLEM
Training Data That Never Sees the Robot
01 / 10
To move safely among people, a robot must perceive nearby pedestrians as individual 3D entities — and predict where they go next.
The problem: the datasets used to train these models don't reflect the robot's real situation.
Fixed top-view cameras
ETH · UCY · SDD
Mounted high on rooftops or drones
A bird's-eye view of a plaza or street
The device never enters the scene
So they never see human-robot interaction
Autonomous-driving data
nuScenes · Waymo · Argoverse
Rich multi-sensor data from a moving car
But car and pedestrians use separate roads
They rarely come into close contact
Neither setting matches a robot in a crowd

## Slide 3
MOTIVATION
Interaction Only Appears Up Close
02 / 10
Interaction is real
Human-robot interaction studies show a robot's
motion changes how nearby people walk — and the
effect is strongest when robot and pedestrians
share the same space, up close.
WHAT WE NEED
To study and model that behavior, we need data
collected while a robot actually moves through
crowds — not from a camera bolted to a building.
Prior robot datasets came close — but each had a gap
STCrowd
Sensors kept at a fixed position →
scenes barely varied.
JRDB
Not organized into trajectories; sensors
not fully time-synchronized → limits fusion.
SiT
is designed specifically to
fill these gaps.

## Slide 4
CONTRIBUTIONS
What SiT Delivers
03 / 10
01
Real crowd trajectories
Large-scale real-world pedestrian trajectories
gathered as a robot navigated crowded indoor and
outdoor scenes — interiors, campuses, crosswalks,
walkways.
02
Rich prediction context
Enables prediction with rich context: appearance
features, the robot's own ego-motion, and semantic
map data around each pedestrian.
03
Synchronized + mapped
Precise time synchronization across all sensors via
centralized triggering makes fusion practical, plus
multi-layered semantic maps for indoor and outdoor
scenes.
04
Unified benchmark
A curated benchmark spanning 3D detection, 3D
multi-object tracking, trajectory prediction, and
end-to-end motion forecasting — all released
publicly.

## Slide 5
DATA COLLECTION
A Sensor-Rich Robot in the Crowd
04 / 10
Clearpath Husky UGV — remotely operated through downtown Seoul
2×
Velodyne
16-ch LiDAR
5×
Basler cameras
360° view
2×
IMU
RTK
positioning
Precise time synchronization
PPS generator
LiDAR
cameras
IMU
A pulse-per-second trigger aligns every sensor in time, making camera–LiDAR fusion reliable.
Robot ego-motion
Pose from RTK outdoors and
LiDAR-inertial SLAM indoors —
needed to compensate ego-motion
when forming trajectories and to
align the maps.
Maps & annotations
12-layer semantic maps from point
clouds. 3D cuboids labeled at 5 Hz,
interpolated to 10 Hz; 2D boxes
share IDs. Faces & plates blurred.

## Slide 6
DATASET & BENCHMARK
Sixty Scenes, Four Benchmarks
05 / 10
Dataset scale
60
scenes
60K
images
12K
point clouds
≈ 470K 2D annotations · ≈ 320K 3D annotations
Clip structure
20 s
of sequential data at 10 Hz
→ 9 s of trajectory, represented as pose vectors.
On top of this data, the paper defines four benchmarks.
Perception benchmarks
1 · 3D pedestrian detection
AP on center distance @ 0.25 / 0.5 / 1 / 2 m
2 · 3D multi-object tracking
Standard MOT metrics (sAMOTA, AMOTA, MOTA…)
Forecasting benchmarks
3 · Trajectory prediction
2 s of past → 7 s ahead, ADE / FDE over best-of-K
4 · End-to-end
Raw sensors → future bounding boxes & trajectories

## Slide 7
KEY RESULT
It Captures the Interaction — and Maps Help
06 / 10
The data analysis confirms SiT captures exactly the close human-robot interaction it set out to.
Where pedestrians appear (relative to ego)
SiT — close, all directions
Waymo / nuScenes — off to the side
Space-sharing + within-2 m instances
SiT
far more
nuScenes / Waymo / Argoverse
Semantic map improves prediction
0.52
ADE₂₀
0.93
FDE₂₀
Best model NSP-SFM with the map — clearly better than without.

## Slide 8
ABLATION
The Map Helps — Fusion Wins
07 / 10
The most informative comparison: turning the semantic map on and off for trajectory prediction.
Y-Net · with vs without map
ADE₂₀
0.84
no map
0.68
+ map
FDE₂₀
1.88
no map
1.55
+ map
Adding the map lowers both errors.
NSP-SFM · with vs without map
ADE₂₀ 0.63 → 0.52
FDE₂₀ 1.09 → 0.93
↓
↓
map helps in both cases
Detection findings
Camera + LiDAR fusion beats single-sensor models
Voxel backbones beat pillar-based ones
TransFusion (voxel) gives the best detection score

## Slide 9
BY THE NUMBERS
Numbers Worth Remembering
08 / 10
A few numbers worth remembering from the SiT dataset and its benchmark.
60 scenes
about 60K images and 12K point cloud
frames, with ≈470K 2D and ≈320K 3D
annotations.
0.52 / 0.93
best trajectory prediction with the
semantic map: ADE₂₀ and FDE₂₀
(NSP-SFM).
0.53 · 0.61
best camera+LiDAR detection mAP, and
CenterPoint tracking sAMOTA — leading
the benchmark.

## Slide 10
TAKEAWAY
Data From the Crowd, Not the Rooftop
09 / 10
The takeaway is simple
Social navigation needs data that shows the robot up close in the crowd —
not a camera bolted to a building.
What such data must have
To build robots that move safely and gracefully among people, you need
close-crowd trajectories, sensors aligned in time, and the surrounding
scene captured as a map.
SiT is the first to deliver it
SiT is the first dataset to combine all three, with a benchmark spanning
detection, tracking, prediction, and end-to-end forecasting — all publicly
released.
SiT
robot in the crowd
scenes
60
sensors
LiDAR+cam+RTK
maps
12 layers
benchmark
4 tasks
github.com/SPALaboratory/SiT-Dataset