## Slide 1
NeurIPS 2022 · ML4AD Workshop
Woven Planet · Autonomous Driving Planning
CW-ERM
Improving Autonomous Driving Planning with Closed-loop
Weighted Empirical Risk Minimization
front
side
side
rear
Eesha Kumar · Yiming Zhang · Stefano Pini · Simon Stent · Ana Ferreira · Sergey Zagoruyko · Christian S. Perone
Trained open, driven
closed
Behavioral cloning matches expert
actions one step at a time, yet
the policy is deployed closed-loop
where every action shapes future
states.
The mismatch hurts
safety
This open-loop versus closed-loop
gap quietly hurts real-world
driving safety.
A two-stage recipe
Run a policy in a simulator to
find the scenes where it fails,
then upsample exactly those scenes
when training the final policy.
~35% fewer collisions
On a challenging urban dataset it
cuts collisions substantially,
with no differentiable simulator
or costly closed-loop training.
arXiv:2210.02174
github.com/wp-research-uk/cw-erm
Closed-loop benefits, without closed-loop training.

## Slide 2
PROBLEM
Trained open-loop, deployed closed-loop
Cloning the expert's next action
Imitation learning for self-driving is
usually behavioral cloning: the network is
trained to reproduce an expert's next
action.
one-step supervised matching
min E || pi(s) - a_expert ||
open-loop: no feedback from its own acts
It never sees its own consequences
Training is open-loop, so the model never sees the effects
of its actions. But when it drives, every action changes
the future state it will see.
expert (open-loop)
policy drift -> OOD
Small errors compound into OOD
Small prediction errors accumulate, pushing the car into
out-of-distribution situations it was never trained on.
The metrics that matter are invisible
Collisions are non-differentiable, invisible to the loss, so the policy
looks great open-loop but drives poorly closed-loop.

## Slide 3
MOTIVATION
Closed-loop benefits, without the cost
Prior work puts the sim in the loop
Methods like Urban Driver run a differentiable simulator
directly inside the training loop, using backpropagation
through time.
grad flows through unrolled sim (BPTT)
But it is expensive
It needs a differentiable simulator, it does not scale
well, and it carries the heavy memory cost of unrolling
policies during training.
differentiable sim · poor scaling · memory heavy
On-policy data and oracles cost more
Other approaches collect on-policy data or add extra
human oracles to label behavior, which are slow and
costly to run.
on-policy rollouts · human oracles · slow
A simpler question -> CW-ERM
Can we get closed-loop benefits by using a simulator only
to decide which training scenes matter, with no loss
change and no differentiability?
simulator picks scenes, not gradients

## Slide 4
CONTRIBUTION
Three contributions, one simple idea
3
Three
contributions
A method, an empirical study,
and a theoretical connection
tie the paper together.
1
1 CW-ERM
Closed-loop Weighted ERM
leverages metrics from policy
rollouts to debias the network
and shrink the open-loop to
closed-loop gap.
2
2 Real gains,
cheaply
Evaluated on a challenging
urban driving dataset, it
shows significant closed-loop
improvements with no expensive
closed-loop training.
3
3 A theoretical
link
It connects this reweighting
to the classic family that
corrects covariate shift
through density-ratio
estimation.
Use the simulator to reweight the training data, and leave the loss and the network untouched.

## Slide 5
METHOD
Train, simulate, then upsample failures
Three stages, and strikingly simple
1
Train identification
policy
standard ERM behavioral
cloning
>
2
Roll out in the
simulator
collect closed-loop costs
(collisions)
>
3
Retrain, upsample
failures
weighted ERM on the error set
Failing scenes -> upsample by w
Every scene with a positive cost, meaning the policy
failed, goes into an error set. The final policy is
retrained with weighted ERM, upsampling those scenes by a
factor w.
cost(scene) > 0 -> error set, x w
Almost the same objective
Nearly identical to behavioral cloning, with a single
weighting term driven by closed-loop failures.
Two tricks, no differentiable sim
Early-stop the ID policy so the error set is not depleted; upsample (not
reweight) for stability; any non-differentiable metric works.

## Slide 6
DATASET / BENCHMARK
Real urban driving, at fleet scale
A proprietary real-world fleet dataset
Collected from the company's self-driving vehicles on challenging urban
missions in San Francisco and Palo Alto.
San Francisco
Palo Alto
Trajectories plus HD maps
Recorded trajectories of the ego vehicle and surrounding
agents, together with high-definition maps.
Diverse, difficult scenarios
Stopping behind a lead car, intersections, dense traffic
with pedestrians and cyclists; most scenes 11-13 s, up to 30
s.
Trained at scale, simulator open-sourced
180 h
training
60 h
validation
60 h
test
closed-loop sim + metrics released

## Slide 7
KEY RESULT
Fewer collisions across the board
Up to ~35% fewer collisions vs the best baseline
~35%
fewer on some metrics
Beats behavioral cloning with ERM and
perturbation, the strongest baseline.
Collisions cut across all zones at once:
front
side
rear
Front collisions
Upsampling front-collision scenes.
14
baseline
>
9
CW-ERM
Side collisions
Upsampling side-collision scenes.
55
baseline
>
47
CW-ERM
Less passive, more stable
Upsampling side collisions also reduces
rear collisions: the policy becomes less
passive, not gaming one number.
variance lower than baseline

## Slide 8
ABLATION STUDY
How to target the right scenes
Single metric vs a Pareto balance
Targeting one metric alone gives the
biggest gain on it; combining metrics
trades off, tracing a Pareto front.
side
front ->
+rear
Front + side + distance works; +rear hurts
Adding rear collisions causes a clear regression, traced
to false positives from log-replayed agents that do not
react in the sim.
rear metric -> non-reacting replay agents
Early-stopping budget K
The identification policy is stopped early. The budget K
controls how full the error set stays.
K = 10
best, single metric
K = 20
best, multi-metric
Upsampling factor peaks near 50
Gains improve up to w around fifty, then
side collisions rise again, echoing
saturation in Just Train Twice.
w ~ 50
side coll.
upsampling w ->

## Slide 9
HEADLINE NUMBERS
The impact in one place
Front collisions, against the strongest baseline
14 -> 9
front collisions
~36%
reduction
Upsampling front-collision scenes drives the largest single-metric drop.
Distance-to-reference & side
35 -> 28
dist-to-ref (~20%)
55 -> 47
side collisions
Overall improvement & best factor
~35%
on some metrics
w ~ 50
best upsampling
Training budget
180 h train · 60 h validation · 60 h test
final policy: 40 epochs

## Slide 10
TAKEAWAY
Simpler, and safer, planners
No diff sim, no human, no CL training
You do not need a differentiable simulator, a human in the
loop, or expensive closed-loop training to get closed-loop
benefits.
Run once, note failures, upsample,
retrain
Just run the policy once in a simulator, mark the scenes where
it fails, upsample those scenes, and retrain the final policy.
Significant, latency-free, any metric
The recipe delivers significant collision reductions, works
with any closed-loop metric, and adds no inference latency.
A clean theoretical story
Weighting scenes by failure is closely connected to correcting
covariate shift through density-ratio estimation.
front
side
rear
CW-ERM · Closed-loop Weighted ERM · Woven Planet · NeurIPS 2022